## Slide 1
VLSI CMOS
4 BIT DIVIDER
CIRCUIT DESIGN
GVHD: TS. Phạm Văn Khoa
Thành viên nhóm:
  Phạm Quốc Thắng – 18161153
  Trần Trung Thắng - 18119121
  Đinh Nhật Khang - 19119099
  Bùi Chí Ngoan - 18119099
  Huỳnh Khánh Duy - 19110981
  Trần Huy Khang - 19119101
90nm Technology

## Slide 2
Phân công công việc | Transistor count
Phạm Quốc Thắng | Tìm hiểu các cổng logic cơ bản
Trần Trung Thắng | Tìm hiểu Tranmisstion gate, Mux
Đinh Nhật Khang | Tìm hiểu Carry Look Ahead Adder
Bùi Chí Ngoan | Tìm hiểu FlipFlop D
Huỳnh Khánh Duy | Tìm hiểu SynCounter 4 bit
Trần Huy Khang | Nguyên lý hoạt động Divider
VLSI CMOS
4 BIT DIVIDER
CIRCUIT DESIGN
90nm Technology

## Slide 3
Mục tiêu
Hiểu rõ về nguyên lý hoạt động của mạch chia 4 bit
Mô phỏng được hoạt động của mạch bằng ứng dụng Cadence trên công nghệ 90nm
Đánh giá được hoạt động, độ trễ lan truyền và công suất tiêu thụ của mạch

## Slide 4
Outline
Tổng quan về các cổng logic
Multiplexer
Carry Look Ahead Adder
FlipFlop D
Counter
4 Bit Divider
Ứng dụng và đánh giá

## Slide 5: Các cổng logic chủ yếu:
Cổng NOT
Cổng NAND
Cổng XOR
Cổng AND
Cổng OR

## Slide 6: NOT GATE
Kí hiệu:
Bảng trạng thái:
Dạng sóng:

## Slide 7
Tp=6.274 (ps)
TpLH=6.54 (ps)
TpHL=6.008 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 8
+
Power Consumption

## Slide 9: NAND GATE
Kí hiệu:
Bảng trạng thái:

## Slide 10
Tp=9.76 (ps)
TpLH=9.34 (ps)
TpHL=10.28 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 11
+
Power Consumption

## Slide 12: AND GATE
Kí hiệu:
Bảng trạng thái:

## Slide 13
Tp=21.83 (ps)
TpLH=21.85 (ps)
TpHL=21.80 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 14
+
Power Consumption

## Slide 15: NOR GATE
Kí hiệu:
Bảng trạng thái:

## Slide 16
Tp=11.06 (ps)
TpLH=11.4 (ps)
TpHL=10.71 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 17
+
Power Consumption

## Slide 18: OR GATE
Kí hiệu:
Bảng trạng thái:

## Slide 19
Tp=25.45 (ps)
TpLH=24.76 (ps)
TpHL=26.14 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 20
+
Power Consumption

## Slide 21: XOR GATE
Kí hiệu:
Bảng trạng thái:

## Slide 22
Tp=9.88 (ps)
TpLH=9.83 (ps)
TpHL=9.93 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 23
+
Power Consumption

## Slide 24
Chart: 
| Not | Nand | And | Nor | Or | Xor
Propagation Delay | 6.27 | 9.76 | 21.83 | 11.06 | 25.45 | 9.88
(
(ps)

## Slide 25
Chart: Power Consumption (1V,100Mhz)
| Not | Nand | And | Nor | Or | Xor
Propagation Delay | 84.42 | 151.94 | 278.78 | 170.91 | 349.47 | 257.6
(nW)

## Slide 26
Tranmisstion gate

## Slide 27
Multiplexers 2 to 1
Tranmisstion gate Mux 2 to 1
Schematic
Symbol
Wave form

## Slide 28
Tp (ps)
TpLH=13.4 (ps)
TpHL=16.7 (ps)
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 29
Power Consumption

## Slide 30: Full Adder 1 bit
Full Adder 1 bit
Sum = A⊕B⊕Cin
in
Cout= (A⊕B) & Cin | (A & B)

## Slide 31: Full Adder 4 bit
Propagation delay = n bit x TpFA

## Slide 32: Full Adder 4 bit

## Slide 33: Full Adder 4 bit

## Slide 34: Full Adder 4 bit

## Slide 35: Full Adder 4 bit

## Slide 36: Full Adder 4 bit

## Slide 37: Full Adder 4 bit

## Slide 38: Full Adder 4 bit

## Slide 39: Full Adder 4 bit
Schematic
Symbol

## Slide 40
Wave form
1
0
0
0
0
1
1
1
1
0
0
0
1
1
1
1
0
1
1
0
0
0
1
0
1
0

## Slide 41
Tp= 55.51 ps
TpLH= 62.18 ps
TpHL= 48.83 ps
Propagation delay
Cout Output
Vdd = 1V f = 100Mhz

## Slide 42
S3 Output
S2 Output
TpLH= 94.14 ps
TpHL= 70.32 ps
Tp= 82.23 ps
Tp= 70.09 ps
TpLH= 76.46 ps
TpHL= 63.72 ps
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 43
TpHL= 77.02 (ps)
TpHL= 22.42 (ps)
TpLH= 76.39 (ps)
TpLH= 41.42 (ps)
Tp= 76.71 ps
Tp= 31.92 ps
S1 Output
S0 Output
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 44
Power Consumption

## Slide 45
Master
Slave
D – Flip Flop
Master – Slave D flipflop

## Slide 46
D – Flip Flop

## Slide 47
Propagation delay
Tp=100.58 (ps)
TpLH=87.67 (ps)
TpHL=113.5 (ps)
Vdd = 1V f = 100Mhz

## Slide 48
Power Consumption

## Slide 49
D – Flip Flop

## Slide 50
Propagation delay
Tp=109.89(ps)
TpLH=96.81 (ps)
TpHL=122.98 (ps)
Vdd = 1V f = 100Mhz

## Slide 51
Power Consumption
+

## Slide 52
Truth table
Block diagram
Master-slave D flip-flop with clear input

## Slide 53
Schematic
Symbol

## Slide 54
Wave form

## Slide 55
Propagation delay
Tp= 102.25 ps
TpLH= 89.20 ps
TpHL= 115.30 ps
Vdd = 1V f = 100Mhz

## Slide 56
+
Power Consumption

## Slide 57
Synchronous 4-Bit Up Counter
0
1
1
Q0 = D
0
1
Q1 = D
1
1
0
1
1
1
0
0
1
1
1
0

## Slide 58
Synchronous 4-Bit Up Counter
Schematic

## Slide 59
Schematic
Wave form

## Slide 60
Propagation delay
Tp=117.01 (ps)
TpLH=105.46 ps
TpHL=128.56 ps
Q0 Ouput
Vdd = 1V f = 100Mhz

## Slide 61
Tp=115.59 (ps)
TpLH=103.58 ps
TpHL=127.60 ps
Q1 Output
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 62
Tp= 115.87 ps
TpLH=104.05 ps
TpHL=127.68 ps
Q2 Output
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 63
Tp= 110.25 ps
TpLH=97.74 ps
TpHL=122.75 ps
Q3 Output
Propagation delay
Vdd = 1V f = 100Mhz

## Slide 65
Power Consumption
+

## Slide 66
4 – bit Divider
A1
A0
A3
A2
S1
S0
S3
S2
1
0
)
1111 - 0111 = 1111 + 1001
= 11000
……

## Slide 67
4 – bit Divider
Schematic
Symbol

## Slide 68
1
0
1
0
0
0
1
1
1
1
0
0
0
1
1
1
0
0
0
1
1
1
1
1
1
1
1
1
0
0
1
0
1
0
1
0
1
1
0
1
0
1
A = 1 1 1 1

## Slide 69
Propagation delay
Tp=115.92 (ps)
TpLH=102.89 (ps)
TpHL=128.94 (ps)
Thương (Q)
Vdd = 1V f = 100Mhz

## Slide 70
Propagation delay
Tp=123.82 (ps)
TpLH=115.15 (ps)
TpHL=132.49 (ps)
Số dư (R)
Vdd = 1V f = 100Mhz

## Slide 71
Power Consumption
+

## Slide 73
Chart: Propagation delay
| Mux 2 - 1 | CLA Adder | Flipflop D | Counter | 4 bit Divider
Column1 | 15.05 | 82.23 | 100.58 | 117.01 | 123.82
(ps)
( Vdd = 1V f = 100Mhz )

## Slide 74
Chart: Power consumption (Vdd = 1V)
| Mux 2 - 1 | CLA Adder | Flipflop D | Counter | 4 bit Divider
50Mhz | 0.076 | 4.6 | 1.53 | 4.59 | 15.24
100Mhz | 0.147 | 9.31 | 2.85 | 9.15 | 24.2
500Mhz | 0.79 | 38.38 | 12.7 | 38.82 | 96.55
(uW)

## Slide 75
Đánh giá và ứng dụng
Tốc độ hoạt động của mạch chia phụ thuộc vào tốc độ xung clock và thời gian thực hiện chưa được tối ưu
Công suất tiêu thụ khá cao
Ứng dụng trong thiết kế ALU ( phép chia 2 số 4 bit )

## Slide 76
Tài liệu tham khảo
CMOS VLSI Design: A Circuits and Systems Perspective (pub.ro)
INTERNATIONAL JOURNAL OF ENGINEERING SCIENCES & RESEARCH TECHNOLOGY : http://www.ijesrt.com/issues%20pdf%20file/Archives-2015/February-2015/59_DESIGN%20AND%20IMPLEMENTATION%20OF%20SERIAL%20DIVIDER%20USING%20180NM%20PROCESS%20TECHNOLOGY.pdf
Carry Look Ahead Adder | 4-bit Carry Look Ahead Adder | Gate Vidyalay

## Slide 77
THANKS FOR WATCHING